## Slide 1: Tick Tock
Synchronize mbeds
Team 7 Lin Li and Shuo Qin
njustlilin@gmail.com
sherry.qin12@gmail.com

## Slide 2: What is it?
Vmaster
Vslave
GND
gnd
TX
Rx
Rx
Tx

## Slide 3: Theory Behind (IEEE 1588 standard)
Master
Slave
Sync Request
T1
t2
Msg contains with info of T1
t2, T1
Delay_Req Msg
T1,t2,t3
Msg contains with info of T4
T4
T1,t2,t3, T4
MeanDelayPath =
((t2-T1)+ (T4-t3))/2
OffsetCorrection =
(t2-T1) - MeanDelayPath

## Slide 4: How to Implement it?
Sampling Method
  Every 10 second perform re-sampling and re-calculating
  Use interrupt of timer to ensure the function in task queue get execute at the right time
Coding
  Critical structure
  Critical functions

## Slide 5: Critical Structure
typedef struct timeval {
  unsigned int tv_sec;
  unsigned int tv_usec;
  } tv;
typedef struct coeffient {
  int Offset_sec;
  int Offset_usec;
  int off_persec;
  double Drift;
  tv y [10];
  tv x [10];
  } coeff;

## Slide 6: Critical Functions
getTime(struct timeval *tv)
  Master: return local clock value
  Slave: return estimate of global time
runAtTime(void) (*schedFunc)(void),struct timeval *tv)
  Master: run a function at a scheduled time with local clock
  Slave: run a function at a scheduled time with “global time”
runAtTrigger(void) (*trigFunc)(struct timeval *tv)
  Response with trigger function when trigger condition occurs

## Slide 7: How well the system is?
6-hour-data-logging
  Master-Slave differences and actual exe time
Max abs difference: 2109us
Min abs difference : 0
Mean abs difference: 51.2143us

## Slide 8: How well the system is? (Allan Variation)
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
offset difference | 18 | 50 | 60 | 79 | 119 | 85 | 17 | 15 | 48 | 43 | 32 | 28 | 4 | 250 | 363 | -8

## Slide 9: Improvements To Be Considered
Temperature control:
  Compensation for calibration